# ACE INDUSTRIAL PRODUCTS

# 5043 Farlin Avenue

# St. Louis, MO  63115

www.aceindustrialproducts.com

# Phone:	314-679-2540

# Fax:		314-385-5178

| Model 73-100 | Portable Fume Extractor |
| --- | --- |
| Ace Industrial Products of St. Louis, MO. manufactured self contained, high vacuum fume extractor constructed of 14 and 16 gauge powder coated semi gloss finish, cold rolled steel. Unit capable of exhausting 113 CFM with filters in place through a 7 amp, 120v single phase vacuum motor. Unit includes built in spark trap and accepts 1” of pre-filtration with a minimum of 3.2 square feet of filter media and main filter with a minimum of 53 square feet of filter media. Unit includes 10 feet of flexible extraction hose, 28” flexible steel extraction tube with 12” slot nozzle and magnetic base, LED filter status light, carry handle, |
| Motor | 7 Amp 120 Volt Single Phase |
| Airflow | 113 cfm |
| Decibels | <85 db |
| Construction | 14 & 16 GA. Cold Rolled Steel w/ finger latching, gasketed filter access |
| Length | 24” |
| Height | 17” |
| Width | 12” |
| Weight | 40 lbs. |
| Capture | 10 foot flexible hose, 12” slot nozzle on flexible tube with magnetic base |
| Primary Pre Filter | 12” x 12” x 1” Multi-Pleat, Cotton / Synthetic Media, 3.2 Sq. Ft media surface rated at 40% ASHRAE efficiency (alternatives available – consult filter and parts guide) |
| Primary Main Filter | 12” x 12” x 11.5” High Capacity Multi-Pleat in Particle Board Frame, 53 sq. ft. media surface rated at 95% ASHRAE efficiency (alternatives available – consult filter and parts guide) |
| Flammability | Class 2, UL Standard 900 |
| Options | Dual Operator T- Connector |
| Warranty | Two Year Limited |
| Source | Made in USA (St. Louis, MO) |